## Slide 1: Networking
Semester III

## Slide 2: Sampling

## Slide 3: Sampling
The aim of sampling is to convert an analog signal into a set of discrete values or snapshots.
A set of signals at specific time intervals, say , is obtained from the signal.

## Slide 4: Sampling
Any analog signal can be represented as weighted sin waves.
Nyquist criteria:
  where T is time period.
  where f is frequency.
is known as the Nyquist rate.

## Slide 5: Nyquist Rate
Samples per second or sampling rate,
Human speech ranges from 30Hz-3.4kHz.
The sampling rate must be greater than 6.8kHz, so 8kHz.
So if there are 10 bits per sample, the data rate is 80kbps or 10kBps.

## Slide 6: Pulse Code Modulation (PCM)
Quantization is the process of deriving an approximate value from the samples obtained from an analog signal.
The process of sampling and quantization together is called pulse code modulation or PCM.
It changes analog pulses to discrete vaules with which the computer can work.

## Slide 7: Line coding

## Slide 8: NRZ-L (Non Return to Zero – Level)
+V volt is transmitted if 1, -V volt is transmitted if 0.
If the average sample value received is positive, it is considered 1, if sample value is negative it is considered 0.
For long streams of 0s or 1s, synchronization is lost.

## Slide 9: NRZ-I (Non Return to Zero – Inverse)
Transition if 1 is transmitted.
No transition if 0 is transmitted.
Loss of synchronization during long stream of 0s.

## Slide 10: RZ (Return to Zero)
Transmits a zero sample after each bit.
In this way synchronization is maintained but due to the presence of three states, it is more error prone.

## Slide 11: Manchester Coding
Transmits bit for half length of the sample and alternate bit for the next half sample.
There is a transition every half sample so synchronization is not lost.
But uses double the bandwidth.

## Slide 12: Differential Manchester
After every transmission, there is a transition.
There is a transition at half-length if 0, no transition at half-length if 1.
Guarantees synchronization but twice the bandwidth is required.

## Slide 13: Wireless transmission

## Slide 14: Modulating Sin-wave Carrier
A sin wave is represented as,
Amplitude modulation: is changed according to bit value.
Frequency modulation: is changed according to bit value.
Phase modulation: is changed according to bit value.

## Slide 15: Amplitude Shift Keying (Binary, BASK)
Amplitude 1 is assigned to bit 1 and amplitude 0 is assigned to bit 0.
So 1 corresponds to signal .
And 0 corresponds to signal .

## Slide 16: Frequency Shift Keying (Binary, BFSK)
Frequency is assigned to bit 1 and frequency is assigned to bit 0.
So 1 corresponds to signal .
And 0 corresponds to .

## Slide 17: Phase Shift Keying (Binary, BPSK)
Phase 0 is assigned to bit 0 and phase is assigned to bit 1.
So 1 corresponds to signal .
And 0 corresponds to signal .

## Slide 18: Phase Shift Keying (4-ary, QPSK)
In QPSK, two bits are taken at a time and assigned different phases.
Phase is assigned to 00.
Phase is assigned to bit 01.
Phase is assigned to bit 11.
Phase is assigned to bit 10.

## Slide 19: Phase Shift Keying (8-ary, 8PSK)
In 8PSK, 3 bits are taken at a time and assigned different phases.
Phase is assigned to 000.
Phase is assigned to bit 001.
Phase is assigned to bit 011.
And so on till phase is assigned to bit 100.